## Slide 1: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
Power of 10bit-multipler
187.2048 nw

## Slide 2: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
Power of 10bit-adder
54.6066 nw

## Slide 3: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
Verilog of 10bit-adder
XOR3D1 * 1
FA1D0 * 8
AN2XD1 * 1
CKXOR2D1 * 1
DFCNQD1 * 10

## Slide 4: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
XOR3D1
FA1D0

## Slide 5: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
AN2XD1
CKXOR2D1

## Slide 6: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
DFCNQD1

## Slide 7: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
Power of 10bit-adder by TSMC libraries (average leakage power)
3.05183 *1 + 5.51902 *8 + 0.94373 *1 + 2.16637 *1 + 2.37778 *10
= 74.09189 nw
Power of 10bit-adder by TSMC libraries (min leakage power)
2.45036 *1 + 4.90338 *8 + 0.46456 *1 + 2.09378 *1 + 1.29048 *10
= 57.14054 nw
Power of 10bit-adder by TSMC libraries (max leakage power)
3.62782 *1 + 6.21911 *8 + 1.40683 *1 + 2.3038 *1 + 3.23731 *10
= 89.46443 nw

## Slide 8: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
XOR3D1
FA1D0

## Slide 9: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
AN2XD1
CKXOR2D1

## Slide 10: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
DFCNQD1

## Slide 11: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
Power of 10bit-adder
54.6066 nw -> 358.2628pw

## Slide 12: 14. A 510nW, 0.41V Low-Memory, Low-Computation Keyword Spotting Chip using Serial FFT based MFCC and Binarized Depthwise Separable Convolutional Neural Network in 28nm CMOS (2020 ISSCC)
Power of 10bit-MFCC-compute-module
1.0510 uw -> 44.537 nw