## Slide 1: Modification I: Post-proces Engine
#MUL in Convolution/FC
#MUL in Post Process
One-time BN/Bias/Act. Function/Element Process can be pipelined after convolution/FC calculation.
Rest post process are computed by accessing the features
from FMemory individually.
Save 32 FP multipliers and adders

## Slide 2: Modification I: Post-process Engine
#MUL in Convolution/FC
#MUL in Post Process
One-time BN/Bias/Act. Function/Element Process can be pipelined after convolution/FC calculation.
Rest post process are computed by accessing the features
from FMemory individually.
Save 32 FP multipliers and adders

## Slide 3: Modification II: CRS Decoding
(c) Shift (4-16 decoder) before And : 32 4-16 decoders
(d) PE IDX Shift and IDX Set: 1 5-32 decoders
Save 16x decoding logic and intermediate result buffer (8.4x in Synthesis)

## Slide 4: Debug I: Clock gating
Computing multiplication in one MAC of Dual PE or Post-process Engine:
The adder logic in the diagram will inverse along with the multiplier output.
Add another ADD_SRC1 register to gate the adder.

## Slide 5: Debug II: Dual PE Enable Signal
When processing FC/Conv without sparsity, the PE array receives synchronous PE enable signals (MUL_EB and ADD_EN).
The randomly distributed conflicted weights require asymmetric PE Enable signals.

## Slide 6: DLA SoC A
CPU can not access DRAM directly;
Data on DRAM <-> DLA GB
<-> CPU;
The SoC must access the DLA on-chip buffer.

## Slide 7: DLA SoC B
CPU accesses DDR directly through AXI-4 and PHI bus.
CPU accesses DLA directly through AXI-4 and AXI-DLA bridge.
DLA accesses DDR directly through PHI bus.

## Slide 8: DLA Interface
Multiplex bus as Data and Address bus;
MOSI and MISO control signals indicate data transfer direction and connect with off-chip interface.

## Slide 9: DDR Rate
DDR | Bus Clock (MHz) | Internal Rate (MHz) | Transfer Rate (MT/s) | Voltage
DDR | 100-200 | 100-200 | 200-400 | 2.5
DDR2 | 200-533 | 100-266 | 400-1066 | 1.8
DDR3 | 400-1066 | 100-266 | 800-2400 | 1.5
DDR4 | 800-1200 | 200-300 | 1600-5067 | 1.2

## Slide 10: Next Plan
64-bit or 32-bit data bus is suitable for off-chip feature/weight access: modify the 256-bit input/output bus to 64/32-bit inout bus.
Fix the DDR-DLA PHI interface.
Time Schedule | 
RTL Freeze | 3.12
Simulation with dummy data | 3.20
Mapping first LSTM/CNN | 4.15
Backend | 5.15

## Slide 11
2019.3.8

## Slide 12: Debug I: Padding
Zero Padding: No storage required but calculated.
Bug: Padding Enable sets to high (send 0 to PE) when Feature Address Counter starts counting (send F0 to PE).
Fix: Delay the feature address until Padding Enable sets to low.
  Add a padding state to the COMP FSM.

## Slide 13: Debug II: Conv Enable near Computing Completion
(a): Ideal case: high MAC utilization.
(b): W1*A4 W2*A5 is useless. Low MAC utilization when gating
Do not occur in Conv 2x1.
Lower MAC utilization with larger weight size.

## Slide 14: DDR3 Interface

## Slide 15: DDR3 Write Sequence

## Slide 16: DDR3 Read Sequence